Heat Exchange in Mixtures

By determining the heat exchange in mixtures we can calculate many useful factors such as the specific heat capacity of a substance, its mass, or its final temperature.

Sample Problem:  What mass of copper at 87.0 °C, when added to 300 g of water at 17.0 °C, would yield a final temperature of 26.0 °C?  Assume that the heat exchange is 100% efficient.

Solution:

- THINK about what is happening to both:

- The final temperature of the mixture must be higher than the cold substance but lower than the hot substance.

- The cold substance gains thermal energy, the hot substances loses thermal energy.

- To calculate (ΔT) we must consider:

Colder substance (ΔT) =

Warmer substance (ΔT) =

- Final solution to mixture problem:

Sample Problem 2:  Heavy metal shots having a mass of 100 g are heated until they reach a temperature of 100°C.  The shots are then quickly transferred to a beaker containing 100 g of water at 20°C.  The contents are gently stirred until an equilibrium temperature of 22.31°C is reached.  What is the specific heat capacity of the shots?  Assume that this thermal energy transfer is 100% efficient.